## Slide 1: Transient Fault Detection and Recovery Mechanisms in μC/OS-II
Chengrui He, Li Zhang, Gang Wang, Ziqi Zhen, Lei Wang
Beihang University

## Slide 2: Transient Fault
Transient fault could sometimes happen
  bit reverse
Satellites
Hospitals
…

## Slide 3: Existed Methods To Detect Transient Fault
Hardware-based solutions
  detect most of the faults
  higher cost, lower flexibility
Software-based solutions
  the ECCA signature algorithm (Z.Alkhalifa et al.)
  a pure software-based CFCSS algorithm (Nahmsuk Oh et al.)

## Slide 4: We Put Forward ...
a coarse-grained error detection scheme based on function call relationships
  detects illegal jump at runtime
  recover from fault
Notes: In general

## Slide 5: Types Of Illegal Jumps
Jump to a function entry
Jump into a function body

## Slide 6: Our Fault Detection Scheme
Insert detection codes at compilation

## Slide 7: Our Fault Detection Scheme
At the entry of every function
  check if the calling is legal
  get info of the caller dynamically
  check whether the caller and the callee has the calling relationship
Jump to a function entry

## Slide 8: Our Fault Detection Scheme
At the exit of every function
  check if the function was entered from its entry point
  mark at entrance with a flag
  check if the mark exists at exit
Jump into a function body

## Slide 9: More Details - Signature
Each function is assigned a unique signature attribute value Li
Each function is assigned a relationship attribute Si to record which function it might call
For each Li1 of function 1 and Si2 of function 2, exists an operator Op which makes Op(Li1, Si2) == true if and only if function 2 is a caller of function 1

## Slide 10: More Details - Signature
void P() {
A();
B();
}
LiA = 00012
LiB = 00102
LiC = 01002
SiP = 00112

## Slide 11: More Details - Entry
Sin = S;
Lin = L;
L = Li;
if (Li & Sin == 0)
error;
S = Si;
S, L – global variables used to deliver info from the caller
Li, Si – const local attributes mentioned before
Lin, Sin – local variables used to save info of the caller

## Slide 12: More Details - Exit
Entry
Sin = S;
Lin = L;
L = Li;
if (Li & Sin == 0)
error;
S = Si;
Exit
if (Li != L)
error;
S = Sin;
L = Lin;

## Slide 13: Implementation
Get call graph
  open source tools such as Codeviz
Insert detection code
  use compilers such as GCC
  generate & insert automatically

## Slide 14: Recover From Fault
Easiest way – restart module
Better way – restart from checkpoint
  when to save information
    correct
    recent
  for the scheduling module, it could be before a schedule process

## Slide 15: Testing

## Slide 16: Testing
Light-weighted (size, speed)
Not sensitive to system load

## Slide 17: Thank You